## Slide 1: MAXIMIZING SWARM COVERAGE: HUNTING FOR MEMBERS OF A MOVING POPULATION Mary Burbage

## Slide 2: Hunting for Swarms
Mosquito-hunting drone
Automated Fishing Trawler
Image by An Nguyen
Image by An Nguyen

## Slide 3: Coverage Problem
Plan a coverage path for a robot such that it encounters each member of a population of mobile particles in a workspace.
For stationary particles or unconstrained time, full spatial coverage is satisfactory.
With mobile particles and a maximum running time, full spatial coverage may not be sufficient.

## Slide 4: Classic Robotic Coverage
Design a path for the robot that ensures the robot visits within a maximum distance of every point in the workspace
Simplest is a lawn-mowing or boustrophedon path, which guarantees complete spatial coverage [Choset, 2000]

## Slide 5: Robotic Coverage – Previous Work
Find ways to subdivide the space around obstacles and apply a boustrophedon-type path [Hert et al, 1996]
Handle moving or unexpected (e.g. unmapped) obstacles [De Carvalho et al, 1997]
Coordinate search among multiple robots [Ge et al, 2005]

## Slide 6: Robotic Coverage – Previous Work
Manage localization and sensor measurement uncertainty [Das et al, 2011]
Optimize path connecting static waypoints [Soltero et al,, 2014]

## Slide 7: Novelty
Things being searched for can move
Space previously covered can be recontaminated or repopulated
Time is so limited that the whole workspace cannot be searched

## Slide 8: Biasing
Unbiased
Biased

## Slide 9: Modeling Mosquito Distributions
Begin with uniform distribution in square area
Set a map as the background for the area
Simulate movement
  Can move up to 0.4 m/s [Clements, 1999]
  Biased toward greenest area surrounding it plus a random component
  Move once every second
Allow mosquitoes to move 5000 steps before robot begins searching

## Slide 10: Building a Path
Paths may be precomputed, randomly selected during a search, rely on feedback, or be a hybrid
Each step is of a uniform length for a constant robot velocity
Robot’s collection device is one unit (1 m) wide

## Slide 11: Path Options
Boustrophedon
Random Bounce
Square Spiral

## Slide 12: Boustrophedon Simulation

## Slide 13: Random Bounce/Spiral Simulation

## Slide 14: Paths Tested
Boustrophedon
Boustrophedon with spiral
Random bounce
Random bounce with spiral

## Slide 15: Spiral Thresholds
Boustrophedon
Setpoints:
10 to enter Spiral
10 to return to Base
Random Bounce
Setpoints:
9 to enter Spiral
3 to return to Base

## Slide 16: Simulations
Test T = 900 s (enough time for full spatial coverage) and T = 300 s (insufficient time for full coverage)
Run 100 trials of each path
Compare results for spatial coverage and population coverage

## Slide 17: Paths for T=900 s
Boustrophedon covers whole field
Boustrophedon with spiral does not cover whole field
Spiral with random bounce gives more population-focused coverage
Boustrophedon
Random Bounce
Boustrophedon/Spiral
Random Bounce/Spiral

## Slide 18: Comparison for T=900 s
Boustrophedon: μ=84.9%, σ=0.4%
Boustrophedon/ Spiral: μ=79.8%, σ=1.7%
Random bounce: μ=65.9%, σ=2.5%
Random bounce/ Spiral: μ=71.9%, σ=3.8%

## Slide 19: Paths for T=300 s
Boustrophedon covers a small solid area
Boustrophedon with spiral using a wider spacing to give more even coverage
Random bounce with spiral dwells in high population areas
Boustrophedon
Random Bounce
Boustrophedon/Spiral
Random Bounce/Spiral

## Slide 20: Comparison for T=300 s
Boustrophedon: μ=31.2%, σ=0.5%
Boustrophedon/ Spiral: μ=35.0%, σ=3.0%
Random bounce: μ=31.2%, σ=2.8%
Random bounce/ Spiral: μ=32.5%, σ=3.5%

## Slide 21: Results
When there is time to cover the whole space, full spatial coverage gives the best population coverage
When there is not time to cover the whole space, a policy that dwells in high population areas is better than pure spatial coverage

## Slide 22: Difficulties with Approach
Simulating individuals gives a very noisy stochastic process
Many iterations are required to find the usual performance for a given set of parameters
Any parameter changes require lengthy reevaluation

## Slide 23: Extension and Generalization
Generalize the movement of the population from individuals to probability distribution functions
Divide the workspace into cells with a probability of containing a particle
Treat the motion of particles between cells as a Markov process

## Slide 24: Markov Processes
Series of events with a probabi- lity of moving from one state to another at each step
Probabilities depend only on the current state, not the past
Build a transition matrix

## Slide 25: Markov Processes (con’t)
With a known vector of initial states, can find the probable states at any time t
As t becomes very large the distribution approaches a limit
  with each row of W the same and denoted w

## Slide 26: Environments for Exploration
Uniform Distribution with Sticky Walls
Normal Distribution

## Slide 27: Uniform Distribution with Sticky Walls
Square workspace with boundary walls
Begin with a uniform distribution
Particles in edge cells are more likely to stay in edge cells than move away from edges
Reduction in probability is called a sticking factor s

## Slide 28: Building the Transition Matrix
Moves must be symmetric to represent uniform distribution
Establish a probability of leaving the current cell k
Set the fraction of that probability of moves in a cardinal direction (sk) vs. a diagonal direction (dk) with sk + dk = 0.25k
Build a local probability array

## Slide 29: Building the Transition Matrix (con’t)
Fold array at edges and corners
Apply sticking coefficient
Fill P from N arrays

## Slide 30: Sticky Wall Stationary Distribution
Shape of distribution
Depth depends on s

## Slide 31: Normal Distribution
Square workspace without walls
Center has something that attracts particles
Particles form a 2-D normal distribution
μ in center, σ variable

## Slide 32: Building the Transition Matrix
Split distribution into two independent 1-D normal distributions
Use cumulative distribution function to set stationary distribution for each cell within bounds and normalize
Stationary distribution is not unique to a transition matrix so build a linear programming problem from the constraints

## Slide 33: Linear Programming Problem
Matlab function linprog
Solve Ax=B for x subject to limit and minimization criteria
Set x for values in P matrix
Build A matrix and B vector from problem constraints

## Slide 34: Selecting Variables
Full matrix has variables
Use symmetry of distribution to reduce to variables

## Slide 35: Linear Programming Problem Probability Constraints

## Slide 36: Linear Programming Problem Stationary Distribution Constraints

## Slide 37: Linear Programming Problem Diffusion Constraint and Options
Diffusion rate constraint – probability k of leaving the center cell
Lower limit for all values: 0
Upper limit for all values: 1
Minimization criteria: Use all values
Solve Ax = B with

## Slide 38: Linear Programming Problem Solution
Apply symmetry to fill other half of matrix
Solve problem in each dimension and multiply to extend to 2-D
Fill P matrix

## Slide 39: Model Verification
This series of images demonstrates how the distribution reforms after removing a swath of the population through the center (y = 50 m).

## Slide 40: Path Planning
Offline Planning
  Sets whole plan before starting search
  Executes plan as given
Online Planning
  Either has no starting plan or modifies plan as robot progresses
  Uses feedback

## Slide 41: Path Options
Boustrophedon
Wall-Following
Hybrid
Square Spiral
One-Step Greedy
Two-Step Greedy

## Slide 42: Testing Variations
Sticky Walls | Normal Distrib.
Wall-Following | Square Spiral Out
Boustrophedon | Square Spiral Out to 50%, In to Center
Hybrid | Square Spiral Out to 80%, In to 80%
Square Spiral In | One-Step Greedy
One-Step Greedy | Two-Step Greedy
Two-Step Greedy | 
Parameter | Values Tested
Time T | 300 s, 600 s
Robot velocity | 6 m/s, 9 m/s, 12 m/s
Particle movement k | 0.2, 0.4, 0.6
Removal rate | 0.5, 0.7, 0.9
Row spacing | L/50, L/20, L/10, L/5
Sticking coefficient s | 0.25, 0.5, 0.75
Standard deviation σ | L/20, L/10, L/5, L/2
L is the length of the workspace

## Slide 43: Sticky Wall Simulation

## Slide 44: Normal Distribution Simulation

## Slide 45: Sticky Wall Results - Overall
1. Two-step greedy
2. Hybrid
3. Square Spiral
4. Boustrophedon
5. Wall-Following
6. One-Step Greedy

## Slide 46: Sticky Wall Results – Area Extremes
Lowest speed, shortest time
Highest speed, longest time

## Slide 47: Sticky Wall Results
Row Spacing
Sticking Coefficient
Particle Transition Probability
Removal Rate

## Slide 48: Short-Sighted One-Step Greedy
Robot in blue cell
One-step chooses (1,98) for next move
Two-step chooses (2,97) for next move
0.42
0.58
0.55
0.49
0.66
0.38
0.41
0.59
0.32
0.31
0.48
0.31
0.47
0.25
0.39
0.70
0.07
0.44
0.06
0.37
3
2
1
4
97
98
99
95
96

## Slide 49: Sticky Wall Results
Relative performance of paths is affected by the fraction of the population around the edges
Parameters that keep more at edges favor methods that remain near the walls longer
Parameters that reduce population at edges favor methods with better exploration of the center

## Slide 50: Normal Distribution Extreme Cases
Instantly Reform
Never Reform

## Slide 51: Normal Distribution Results – Overall
1. Two-step greedy
2. One-step greedy
3. Square spiral with 50% return to center
4. Square spiral with 80% thresholds
5. Square spiral out

## Slide 52: Normal Distribution Results Area Extremes

## Slide 53: Normal Distribution Results
Row Spacing
Standard Deviation
Particle Transition Probability
Removal Rate

## Slide 54: Stationary Collection
Consider an immobile collecting robot/device
Located at center of workspace
Can have a constant power source
Assuming mobile robot runs four times per day, T = 21,600 s for stationary device
Normal distribution – can collect 99.9%
Sticky walls – can collect 9.7%
Can be very effective when particles are
attracted toward its location
Image by Malcolm Koo
CC-BY-SA 3.0

## Slide 55: Discussion
Two-step greedy has best results in both environments but also requires most sensing
More steps would lead to better performance but take more computation time
In right conditions, wall following or immobile collector can be feasible

## Slide 56: Conclusions
Investigated a new problem in robotic coverage
Maximize number of moving particles collected from a swarm
Individual simulations with biased particles
Markov process simulations with uniform distribution but with sticky walls
Markov process simulations with normal distribution
Pre-planned paths and feedback-based paths

## Slide 57: Conclusions (con’t)
For sticky walls, relative merit of paths varies with environment and swarm parameters
For normal distribution, relative merit of paths is independent of parameters chosen
Many directions open for further research
  Multiple robots
  Combination environments
  Increased greedy steps
  Obstacles
  Particles that react to the robot
Image by An Nguyen